## Slide 1: MANTRA: AN INTEGRAL REACTOR PHYSICS EXPERIMENT TO INFER ACTINIDE CAPTURE CROSS-SECTIONS FROM THORIUM TO CALIFORNIUM WITH ACCELERATOR MASS SPECTROMETRY
G. Youinou2, R. Vondrasek1, *M. Salvatores2,4, B. Scott1, E. Rehm1,
M. Paul1, R. Pardo1, *G. Palmiotti2, C. Nair1, T. Maddock2, J.K. Nimmagadda3 ,
M. Meyer2, C. McGrath2, S. Kondrashev1, F. Kondev1, G. Imel3, C. Glass2
1 Argonne National Laboratory
2 Idaho National Laboratory
3 Idaho State University
4 CEA-Cadarache
*Originators of the project
Applications of Nuclear Science and Technology Information
Exchange Meeting
August 22‐23, 2011, Washington DC

## Slide 2
Principle of the experiment:
1 – Irradiate very pure actinide material (a few mg) in well-characterized neutron spectra in the Advanced Test Reactor (ATR) at INL
→ 232Th, 235U, 236U, 238U, 237Np, 238Pu, 239Pu, 240Pu, 241Pu, 242Pu, 241Am, 243Am, 244Cm and 248Cm
2 – Measure the atom densities of the transmutation products with Accelerator Mass Spectrometry at the ATLAS facility at ANL
→ detection limit of AMS is orders of magnitude lower than that of standard MS (~10-12)
→ more transmutation products can be measured
→ more neutron cross-sections to be inferred from a single sample
3 – Measure the neutron fluence in the actinide samples
→ 148Nd and 137Cs in 235U monitors
4 – Infer the effective neutron capture cross-sections from results of step 2 and 3

## Slide 3
The relation between measured and inferred quantities is given by the solution to the Bateman equations which, in a 100% pure sample of mass number A, can be expressed as:
= effective neutron capture cross-section
inferred quantities →
measured quantities → relative atom densities NA+1, NA+2,NA+3 … and neutron fluence τ
3
Example of A+1, A+2 and A+3 build-up from successive neutron captures on A
Very good approximation in most cases we are interested in. The correction factors will be taken into account in the actual analyses.

## Slide 4
Relation between measured and inferred quantities
Example of a very pure sample containing essentially (i.e. at least 99%) an isotope of mass number A, but also a few tenths of a percent of other isotopes present as impurities (let’s say A+1, A+2 and A+3).
Contribution from A
Contribution from A+1
Left-over of the initial A+2
N.B.: i.e. we don’t need absolute N

## Slide 5
Relation between measured and inferred quantities
If << the expressions are simpler and the inference is less dependant on the precision of the measurement of the atom densities. Relatively easy with thermal or epithermal neutron spectra ( ~ few 10 to few 100 barns). More difficult with fast neutron spectra ( ~ 1 barn)
→ High neutron fluence
→ High purity samples

## Slide 6
Best sample candidates for ATLAS = Heaviest long-lived isotope in each element (U, Np, Pu, Am, Cm) because A+1, A+2… contamination can be kept at a much lower level. U-235 is added to this list because its chain is only loosely coupled with that of U-238. Pu-244 is not of interest for reactor physics or fuel cycle but has been included because it generates Cm-245 after 2 short beta decays.
For these samples the high sensitivity of ATLAS is an important asset because of a low background
When high background, precision matters more than sensitivity

## Slide 7
~0.5%
~0.5%
measured
calculated
~1%-1.5%
Determination of the neutron fluence by the Nd-148 and Cs-137 method in U-235 monitors

## Slide 8
A Brief Description of ATR

## Slide 9
Samples irradiation in ATR
Three Positions: B9, 10 and 11
Three Neutron filters: → 1 mm Cadmium → 5 mm Boron (70% 10B) → 10 mm Boron (70% 10B)
Irradiation in ATR: Jan.-Dec. 2012
Time of irradiation: → 50 days for Cd-filtered → 100 days for B-filtered

## Slide 10
Samples irradiation in ATR
Actinide sample
Example of a boron filtered setup

## Slide 11
Samples irradiation in ATR – Neutron filters
The Cd neutron filter can be manufactured at the INL.
Ceradyne, Inc identified as proposed vendor for B4C filters (70% 10B)
→ The 2 sets of boron filters are now at INL

## Slide 12
Effect of neutron filters on the neutron spectrum in the samples

## Slide 13
1 mm Cd filter
10 mm boron filter
5 mm boron filter
but instead
= effective neutron capture XS
with Cd filter
with 5mm B
with 10mm B
depends strongly on
MANTRA does not access directly to

## Slide 14
Because of the strong dependence of with regard to
it is important that =
to ensure that the differences between and can be attributed to differences between and
Flux monitors will be used to characterize experimentally
experiment provides
calculation provides
Monitors: S-32, Sc-45, Ti-46, Fe-54, Fe-58, Co-59, Ni-58, Cu-63

## Slide 15
MANTRA Neutron Spectra vs. Advanced Reactor Neutron Spectra
(C. Glass, G. Palmiotti, M. Pope, personal communication)
Gas-cooled fast reactor
Low-moderation PWR
Deep Burn VHTR

## Slide 16
Example of U-238, Pu-242 and Cm-248 samples (100% pure)
 | U8 | Pu9 | Pu0 | Pu1 | Pu2 | Am3 | Cm2
50 days Cadmium | 0.991 | 8E-03 | 2E-05 | 2E-06 | 2E-09 | 2E-11 | 1E-11
100 days Boron | 0.999 | 2E-04 | 7E-08 | 2E-11 | - | - | -
 | Cm8 | Bk9 | Cf9 | Cf0 | Cf1 | Cf2
50 days Cadmium | 0.992 | 7E-03 | 4E-04 | 1E-04 | 8E-06 | 7E-08
100 days Boron | 0.999 | 1E-04 | 3E-05 | 2E-07 | 1E-10 | -
 | Pu2 | Am3 | Cm4 | Cm5 | Cm6 | Cm7
50 days Cadmium | 0.964 | 3E-02 | 9E-04 | 6E-06 | 5E-09 | 4E-12
100 days Boron | 0.999 | 3E-04 | 1E-07 | 2E-11 | - | -

## Slide 17
Experimental data are very scarce above Cm
→ MANTRA will provide valuable experimental data above Cm for advanced fuel cycles
17

## Slide 18
From the atom densities to the neutron cross sections – Analyses Based on the C/E
C/E = 1 → nothing to be done – the nuclear data allow to reproduce the measured results
C/E ≠ 1 → global statistical adjustment of the effective cross sections to bring the C/E as close as possible to 1
The method makes use of:
    “a priori” nuclear data covariance information,
    integral experiments analysis to define C/E values
    integral experiment uncertainties
    sensitivity coefficients obtained via perturbation theory:
The use of the chain rule allows to go down one level from to the actual nuclear parameters characterizing
18

## Slide 19
Planning & Budget
Planning shifted 18 months due to priorities at the Analytical Lab at INL as well as its unexpected shutdown earlier this year
Sample preparation completed by October 2011
Irradiation in ATR scheduled for Jan.-Dec. 2012
PIE (ANL & INL) completed by Dec. 2013
Final Report in March 2014
Summary of INL expenditures by FY
 | FY 2010 | FY 2011 | FY 2012
a) Funds allocated | $368,000 | $346,000 | $346,000
b) Costs accrued | $344,377 | $171,702 | $0
c) Uncosted commitments | $ 20,308 | $6,092 | $0
d) Uncommitted funds (d=a-b-c) | $ 3,315 | $168,206 | $346,000

## Slide 20
Publications
G. Youinou, M. Salvatores, M. Paul, R. Pardo, G. Palmiotti, C. McGrath, F. Kondev, G. Imel, “MANTRA: An Integral Reactor Physics Experiment to Infer Actinide Capture Cross-Sections From Thorium To Californium With Accelerator Mass Spectrometry”, Eleventh International Conference on Nuclear Data for Science and Technology, Jeju Island, Korea, 2010, published in the Journal of the Korean Physical Society, Vol. 59, No. 2, August 2011, pp. 1940-1944
G. Youinou, G. Palmiotti, M. Salvatores, G. Imel, R. Pardo, F. Kondev, M. Paul. “Principle and Uncertainty Quantification of an Experiment Designed to Infer Actinide Neutron Capture Cross-Sections”, INL/EXT-10-17622 (2010), available at www.inl.gov/technicalpublications/Documents/4460753.pdf